## Slide 1
Chapter 9 Network Management
Computer Networking: A Top Down Approach 6th edition Jim Kurose, Keith Ross Addison-Wesley March 2012
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2012
J.F Kurose and K.W. Ross, All Rights Reserved
Network Management
9-<number>

## Slide 2: Chapter 9: Network Management
Network Management
9-<number>
Chapter goals:
introduction to network management
  motivation
  major components
Internet network management framework
  MIB: management information base
  SMI: data definition language
  SNMP: protocol for network management
  security and administration
presentation services: ASN.1
Notes: <number>

## Slide 3: Chapter 9 outline
Network Management
9-<number>
What is network management?
Internet-standard management framework
  Structure of Management Information: SMI
  Management Information Base: MIB
  SNMP Protocol Operations and Transport Mappings
  Security and Administration
ASN.1
Notes: <number>

## Slide 4: What is network management?
Network Management
9-<number>
autonomous systems (aka “network”): 1000s of interacting hardware/software components
other complex systems requiring monitoring, control:
  jet airplane
  nuclear power plant
  others?
"Network management includes the deployment, integration
and coordination of the hardware, software, and human
elements to monitor, test, poll, configure, analyze, evaluate,
and control the network and element resources to meet the
real-time, operational performance, and Quality of Service
requirements at a reasonable cost."
Notes: <number>

## Slide 5: Infrastructure for network management
Network Management
9-<number>
managed device
managed device
managed device
managed device
definitions:
managed devices contain
managed objects whose
data is gathered into a
Management Information
Base (MIB)
managing
entity
data
managing entity
agent
data
agent
data
agent
data
agent
data
network
management
protocol
managed device
agent
data
Notes: <number>

## Slide 6: Network management standards
Network Management
9-<number>
OSI CMIP
Common Management Information Protocol
designed 1980’s: the unifying net management standard
too slowly standardized
SNMP: Simple Network Management Protocol
Internet roots (SGMP)
started simple
deployed, adopted rapidly
growth: size, complexity
currently: SNMP V3
de facto network management standard
Notes: <number>

## Slide 7: Chapter 9 outline
Network Management
9-<number>
What is network management?
Internet-standard management framework
  Structure of Management Information: SMI
  Management Information Base: MIB
  SNMP Protocol Operations and Transport Mappings
  Security and Administration
ASN.1
Notes: <number>

## Slide 8: SNMP overview: 4 key parts
Network Management
9-<number>
Management information base (MIB):
  distributed information store of network management data
Structure of Management Information (SMI):
  data definition language for MIB objects
SNMP protocol
  convey manager<->managed object info, commands
security, administration capabilities
  major addition in SNMPv3
Notes: <number>

## Slide 9: SMI: data definition language
Network Management
9-<number>
Purpose: syntax, semantics of management data well-defined, unambiguous
base data types:
  straightforward, boring
OBJECT-TYPE
  data type, status, semantics of managed object
MODULE-IDENTITY
  groups related objects into MIB module
Basic Data Types
INTEGER
Integer32
Unsigned32
OCTET STRING
OBJECT IDENTIFIED
IPaddress
Counter32
Counter64
Guage32
Time Ticks
Opaque
Notes: <number>

## Slide 10: SNMP MIB
Network Management
9-<number>
OBJECT TYPE:
OBJECT TYPE:
OBJECT TYPE:
objects specified via SMI
OBJECT-TYPE construct
MIB module specified via SMI
MODULE-IDENTITY
(100 standardized MIBs, more vendor-specific)
MODULE
Notes: <number>

## Slide 11: SMI: object, module examples
Network Management
9-<number>
OBJECT-TYPE: ipInDelivers
MODULE-IDENTITY: ipMIB
ipInDelivers OBJECT TYPE
SYNTAX Counter32
MAX-ACCESS read-only
STATUS current
DESCRIPTION
“The total number of input
datagrams successfully
delivered to IP user-
protocols (including ICMP)”
::= { ip 9}
ipMIB MODULE-IDENTITY
LAST-UPDATED “941101000Z”
ORGANZATION “IETF SNPv2
Working Group”
CONTACT-INFO
“ Keith McCloghrie
……”
DESCRIPTION
“The MIB module for managing IP
and ICMP implementations, but
excluding their management of
IP routes.”
REVISION “019331000Z”
………
::= {mib-2 48}
Notes: <number>

## Slide 12: MIB example: UDP module
Network Management
9-<number>
Object ID Name Type Comments
1.3.6.1.2.1.7.1 UDPInDatagrams Counter32 total # datagrams delivered
at this node
1.3.6.1.2.1.7.2 UDPNoPorts Counter32 # underliverable datagrams:
no application at port
1.3.6.1.2.1.7.3 UDInErrors Counter32 # undeliverable datagrams:
all other reasons
1.3.6.1.2.1.7.4 UDPOutDatagrams Counter32 # datagrams sent
1.3.6.1.2.1.7.5 udpTable SEQUENCE one entry for each port
in use by app, gives port #
and IP address
Notes: <number>

## Slide 13: SNMP naming
Network Management
9-<number>
question: how to name every possible standard object (protocol, data, more..) in every possible network standard??
answer: ISO Object Identifier tree:
  hierarchical naming of all objects
  each branchpoint has name, number
1.3.6.1.2.1.7.1
ISO
ISO-ident. Org.
US DoD
Internet
udpInDatagrams
UDP
MIB2
management
Notes: <number>

## Slide 14: OSI Object Identifier Tree
Network Management
9-<number>
Notes: <number>

## Slide 15: SNMP protocol
Network Management
9-<number>
Two ways to convey MIB info, commands:
agent
data
managed device
managing
entity
agent
data
managed device
managing
entity
trap msg
request
request/response mode
trap mode
response
Notes: <number>

## Slide 16: SNMP protocol: message types
Network Management
9-<number>
GetRequest
GetNextRequest
GetBulkRequest
Mgr-to-agent: “get me data”
(instance,next in list, block)
Message type
Function
InformRequest
Mgr-to-Mgr: here’s MIB value
SetRequest
Mgr-to-agent: set MIB value
Response
Agent-to-mgr: value, response to
Request
Trap
Agent-to-mgr: inform manager
of exceptional event
Notes: <number>

## Slide 17: SNMP protocol: message formats
Network Management
9-<number>
….
PDU
type
(0-3)
Request
ID
Error
Status
(0-5)
Error
Index
Name
Value
Name
Value
….
PDU
type
4
Enterprise
Agent
Addr
Trap
Type
(0-7)
Specific
code
Time
stamp
Name
Value
Get/set header
Variables to get/set
Trap header
Trap info
SNMP PDU
Notes: <number>

## Slide 18: SNMP security and administration
Network Management
9-<number>
encryption: DES-encrypt SNMP message
authentication: compute, send MIC(m,k): compute hash (MIC) over message (m), secret shared key (k)
protection against playback: use nonce
view-based access control:
  SNMP entity maintains database of access rights, policies for various users
  database itself accessible as managed object!
Notes: <number>

## Slide 19: Chapter 9 outline
Network Management
9-<number>
What is network management?
Internet-standard management framework
  Structure of Management Information: SMI
  Management Information Base: MIB
  SNMP Protocol Operations and Transport Mappings
  Security and Administration
The presentation problem: ASN.1
Notes: <number>

## Slide 20: The presentation problem
Network Management
9-<number>
Q: does perfect memory-to-memory copy solve “the communication problem”?
A: not always!
problem: different data format, storage conventions
struct {
char code;
int x;
} test;
test.x = 256;
test.code=‘a’
a
00000001
00000011
a
00000011
00000001
test.code
test.x
test.code
test.x
host 1 format
host 2 format
Notes: <number>

## Slide 21: A real-life presentation problem:
Network Management
9-<number>
aging 60’s
hippie
2012 teenager
grandma
Groovy!
?
?
?
?
?
?
?
?
Notes: <number>

## Slide 22: Presentation problem: potential solutions
Network Management
9-<number>
1. Sender learns receiver’s format. Sender translates into receiver’s format. Sender sends.
      real-world analogy?
      pros and cons?
2. Sender sends. Receiver learns sender’s format. Receiver translate into receiver-local format
      real-world-analogy
      pros and cons?
3. Sender translates host-independent format. Sends. Receiver translates to receiver-local format.
      real-world analogy?
      pros and cons?
Notes: <number>

## Slide 23: Solving the presentation problem
Network Management
9-<number>
1. Translate local-host format to host-independent format
2. Transmit data in host-independent format
3. Translate host-independent format to remote-host format
2012 teenager
aging 60’s
hippie
grandma
presentation
service
presentation
service
presentation
service
“Groovy!”
“It is pleasing
to me!”
“It is pleasing
to me!”
“Cat’s pajamas!”
“Awesome, dude!”
!
!
!
!
!
!
!
!
Notes: <number>

## Slide 24: ASN.1: Abstract Syntax Notation 1
Network Management
9-<number>
ISO standard X.680
  used extensively in Internet
  like eating vegetables, knowing this “good for you”!
defined data types, object constructors
  like SMI
BER: Basic Encoding Rules
  specify how ASN.1-defined data objects to be transmitted
  each transmitted object has Type, Length, Value (TLV) encoding
Notes: <number>

## Slide 25: TLV Encoding
Network Management
9-<number>
Idea: transmitted data is self-identifying
  T: data type, one of ASN.1-defined types
  L: length of data in bytes
  V: value of data, encoded according to ASN.1 standard
1
2
3
4
5
6
9
Boolean
Integer
Bitstring
Octet string
Null
Object Identifier
Real
Tag Value Type
Notes: <number>

## Slide 26: TLV encoding: example
Network Management
9-<number>
Length, 5 bytes
Type=4, octet string
Length, 2 bytes
Type=2, integer
lastname ::= OCTET STRING
weight ::= INTEGER
{weight, 259}
{lastname, “smith”}
module of data type
declarations written
in ASN.1
instances of data type
specified in module
Basic Encoding Rules
(BER)
3
1
2
2
h
t
i
m
s
5
4
transmitted
byte
stream
Value, 5 octets (chars)
Value, 259
Notes: <number>

## Slide 27: Network management: summary
Network Management
9-<number>
network management
  extremely important: 80% of network “cost”
  ASN.1 for data description
  SNMP protocol as a tool for conveying information
network management: more art than science
  what to measure/monitor
  how to respond to failures?
  alarm correlation/filtering?
Notes: <number>